## Slide 1
Point Switch Functionality Detection in Railroads
Dharanidharan K (910022104037)
Santhosh Kumar R (910022114002)
Vignesh K (910022106042)
Mentor: Dr. A. Muthumari (SL/AP)
Anna University Regional Campus Madurai

## Slide 2
Introduction
Railway Safety
Railway safety is paramount, and point switches are critical components in guiding trains safely between tracks.
The Problem: Urgent Need
Frequent derailments caused by improper switch alignment pose significant risks. There's a critical lack of real-time monitoring for train pilots, compromising safety. Eg: BALASHORE INCIDENT
Our Solution: Scope of Work
We aim to develop a low-cost, real-time detection system for point switches. This system will utilize LoRa for wireless communication to alert locomotive pilots. Our future vision includes integration with broader automation and IoT systems.

## Slide 3
Objectives & Methodology
Our Core Objectives
Our project aims to:
Detect accurate or inaccurate alignment of railroad point switches in real-time.
Provide immediate wireless alerts directly to train pilots in their cabins.
Significantly reduce the incidence of train derailments, thereby enhancing overall railway safety.
Implementation Methodology
Servo Motor: Utilized for precise control and movement of the switch mechanism.
Inductive Proximity Sensors: Employed to accurately detect the alignment status of the rail tracks.
LoRa Transmitter-Receiver: Enables reliable wireless communication over distances of approximately 1 km for data transmission.
Buzzer Alert: Provides immediate audible warning in the pilot's cabin upon detecting misalignment.
Prototype Testing: Rigorous testing of the developed system to ensure functionality and reliability.

## Slide 4
Results & Discussion
Key Results & Achievements
Successful real-time detection of track alignment.
Wireless transmission functionality tested within a 1 km range.
Immediate pilot notification via LCD, Buzzer, and LED indicators.
Significantly reduced response time compared to manual detection methods.
Acknowledged Limitations
The current system is a prototype, operating at a limited scale.
Further development required for comprehensive weatherproofing.
Challenges associated with large-scale deployment need to be addressed.

## Slide 5
Results & Discussion

## Slide 6
Prototype / Process Developed
Prototype Features
Motorized Point Switch Model
A miniature model of a point switch controlled by a servo motor, enabling precise operation and simulation of real-world rail movements.
Inductive Proximity Sensors
Sensors positioned at the switch junction to accurately detect the physical alignment or misalignment of the rail tracks.
LoRa Wireless Module
An integrated LoRa module facilitating long-range, low-power wireless communication for data transmission.
Cabin Alert System
An alert system comprising an LCD display for text messages, LED indicators for visual cues, and a buzzer for audible warnings within the pilot's cabin.
Process Flow
Train Approaches
As the train approaches the point switch (within approximately 1 km range), the system activates.
Sensor Checks & Data Transmission
The inductive proximity sensors check the alignment of the point switch, and the data is wirelessly transmitted via the LoRa module.
Pilot Receives Alert
The locomotive pilot immediately receives an alert in their cabin, indicating either 'Track Detected' (aligned) or 'Track Not Detected' (misaligned).

## Slide 7
Conferences / Publications
IEEE Conference on Intelligent Transportation Systems.
Naan Mudhalvan 4.0 Hackathon Winner.

## Slide 8
Outcomes / Conclusion
Outcomes
Our project successfully developed a functional prototype that provides real-time wireless alerts for railway point switch alignment, enhancing immediate operational awareness.
Conclusion
The system has the potential to significantly reduce derailments, leading to improved railway safety. It is designed for scalability, allowing for future integration with broader IoT and AI systems for enhanced capabilities.
Future Scope
Future development includes integrating camera modules for visual verification, implementing cloud-based monitoring for centralized data access, and incorporating AI for predictive maintenance to anticipate issues before they occur.